## Slide 1: Kernel Panics :-
Kernel oops:-
In sort an kernel oops is a segment fault in the Linux kernel, The kernel doesn't necessarily have to be panic at this stage, In the some OS's it may lead to destroy only the current program.
Kernel panic :-
A panic is a type of kernel oops but the state of machine was not recoverable, it can only recoverable when the system reboots only.
A oops may become severe panic when it destroys the important processes memory example, init, systemd, ksyslogd..,
Further reading :-
http://venkateshabbarapu.blogspot.com/2012/11/oops-vs-kernel-panic.html

## Slide 2: Creation sources of Panics in Linux Kernel :-
By dereferencing to the NULL pointer at the '0' space, as follow *(int *)0 = 0;
By using the kernel providing call of panic call available in kernel/panic.h (or) linux/panic.h the call is as follows panic("panic message ");
By using the SysRq as follows echo c > /proc/sysrq-trigger

## Slide 3: Result of kernel panic :-
BUG: unable to handle kernel NULL pointer dereference at 00000000
[ 459.577396] IP: training_store+0x45/0x60 [sysfs_example]
[ 459.577542] *pdpt = 00000000157dd001 *pde = 0000000000000000
[ 459.577741] Oops: 0002 [#1] SMP
459.579305] CPU: 0 PID: 2832 Comm: bash Tainted: G WC OE 4.15.0-45-generic #48~16.04.1-Ubuntu
[ 459.579609] Hardware name: innotek GmbH VirtualBox/VirtualBox, BIOS VirtualBox 12/01/2006
[ 459.579831] EIP: training_store+0x45/0x60 [sysfs_example]
[ 459.579980] EFLAGS: 00010292 CPU: 0
[ 459.580115] EAX: 00000011 EBX: f4965378 ECX: f6dee200 EDX: f6de7634
[ 459.580269] ESI: ebae6400 EDI: e42d1be0 EBP: cb815ed4 ESP: cb815ecc
[ 459.580431] DS: 007b ES: 007b FS: 00d8 GS: 00e0 SS: 0068
[ 459.580613] CR0: 80050033 CR2: 00000000 CR3: 2408e8c0 CR4: 000406f0
[ 459.580783] Call Trace:
[ 459.580906] ? 0xf83bf000
[ 459.581031] kobj_attr_store+0x13/0x30
[ 459.581170] ? kobj_attr_show+0x20/0x20
[ 459.581323] sysfs_kf_write+0x35/0x50
NOTE :- In this practice I am using a ubuntu 16.04LTS "32-bits" OS, Please Consider that the Register values/names may vary with your 64-bit operating system.

## Slide 4
459.582593] ? sysfs_kf_bin_read+0xc0/0xc0
[ 459.582968] kernfs_fop_write+0xf1/0x180
[ 459.583309] ? kernfs_vma_page_mkwrite+0x70/0x70
[ 459.583683] __vfs_write+0x1c/0x50
[ 459.584024] vfs_write+0x96/0x1a0
[ 459.584492] SyS_write+0x47/0xb0
[ 459.584853] do_fast_syscall_32+0x7f/0x1d0
[ 459.585234] entry_SYSENTER_32+0x4e/0x7c
[ 459.585580] EIP: 0xb7fa1d05
[ 459.585904] EFLAGS: 00000246 CPU: 0
[ 459.586258] EAX: ffffffda EBX: 00000001 ECX: 08348c08 EDX: 00000006
[ 459.586646] ESI: b7f5bd60 EDI: 08348c08 EBP: 00000006 ESP: bff78c58
[ 459.587006] DS: 007b ES: 007b FS: 0000 GS: 0033 SS: 007b
[ 459.588904] Code: db b9 05 00 00 00 ba 27 00 3c f8 89 d8 e8 34 97 4d db 83 c4 0c 85 c0 74 08 8b 45 08 8b 5d fc c9 c3 68 2d 00 3c f8 e8 fa 55 d1 da <c7> 05 00 00 00 00 00 00 00 00 58 eb e1 8d b4 26 00 00 00 00 8d
[ 459.592476] EIP: training_store+0x45/0x60 [sysfs_example] SS:ESP: 0068:cb815ecc
[ 459.593323] CR2: 0000000000000000

## Slide 5: BREAK-DOWN OF DMESG OF PANIC :-
Reason of panic :-
[ 459.577165] BUG: unable to handle kernel NULL pointer dereference at 00000000
Intruction pointer range :-
[ 459.577396] IP: training_store+0x45/0x60 [sysfs_example]
[ 459.577542] *pdpt = 00000000157dd001 *pde = 0000000000000000
[ 459.577741] Oops: 0002 [#1] SMP :-
Protection bits of the processor.
[ 459.579305] CPU: 0 PID: 2832 Comm: bash Tainted: G :-
Panic occurred at CPU 0 and pid of process is 2832

## Slide 6
[ 459.579831] EIP: training_store+0x45/0x60 [sysfs_example]
[ 459.579980] EFLAGS: 00010292 CPU: 0
[ 459.580115] EAX: 00000011 EBX: f4965378 ECX: f6dee200 EDX: f6de7634
[ 459.580269] ESI: ebae6400 EDI: e42d1be0 EBP: cb815ed4 ESP: cb815ecc
[ 459.580431] DS: 007b ES: 007b FS: 00d8 GS: 00e0 SS: 0068
[ 459.580613] CR0: 80050033 CR2: 00000000 CR3: 2408e8c0 CR4: 000406f0
These are values that stored in the CPU registers at time of occurance of panic in the kernel.
[ 459.580783] Call Trace:
[ 459.580906] ? 0xf83bf000
[ 459.581031] kobj_attr_store+0x13/0x30
[ 459.581170] ? kobj_attr_show+0x20/0x20
[ 459.581323] sysfs_kf_write+0x35/0x50
[ 459.582593] ? sysfs_kf_bin_read+0xc0/0xc0
[ 459.584492] SyS_write+0x47/0xb0
[ 459.584853] do_fast_syscall_32+0x7f/0x1d0
[ 459.585234] entry_SYSENTER_32+0x4e/0x7c
[ 459.585580] EIP: 0xb7fa1d05
[ 459.585904] EFLAGS: 00000246 CPU: 0
These are the call trace back of the kernel panic in the Linux.

## Slide 7: DEBUGGING with Crash :-
The Kernel the you're going to crash is pre compiled with the configuration parameters of:-
CONFIG_RELOCATABLE=y CONFIG_KEXEC=y CONFIG_CRASH_DUMP=y CONFIG_DEBUG_INFO=y CONFIG_MAGIC_SYSRQ=y CONFIG_PROC_VMCORE=y
Then after the kernel build is completed you need to install the kexec-tools and kdump-tools in your Linux operating system.

## Slide 8
After these steps your Linux kernel is ready to collect the kernel crashes
And the crash details are stored in the "/var/crash" folder with date-and-time as folder name.
For kernel build and configuring kdump and kexec .
Then after collecting these kernel crashes you can use the crash utility for debugging the crash kernel.
A good tutorial regarding is as follows :-
http://index-of.co.uk/Reversing-Exploitin/Linux_Kernel_Crash_Book.pdf